## Slide 1: FEED WATER CHARACTERISTICS

## Slide 2: COMMON FEED WATER CHARACTERISTICS
pH: Measures the water's acidity or alkalinity, which affects corrosion and chemical processes within the system.
Hardness: Refers to the concentration of dissolved minerals like calcium and magnesium, which can cause scaling in boilers.
Dissolved Solids (TDS): The total amount of dissolved minerals, salts, and other substances, which can increase operating pressure in RO systems and contribute to scaling in boilers.
Suspended Solids: Fine particles that are not dissolved, such as silt and other impurities, that can cause fouling and blockages.
Dissolved Gases: Gases like oxygen and carbon dioxide can increase corrosion in boiler systems.
Temperature: Impacts the viscosity of the water, affecting production rates in RO systems and heat transfer efficiency in boilers.
Organics: Organic matter can foul membranes in RO systems and contribute to biological contamination in water systems.

## Slide 3
Main parameters in desalination include feed water characteristics (salinity, temperature, turbidity), process-specific parameters like operating pressure and membrane type for reverse osmosis (RO) or heat loss for thermal processes, and post-treatment variables such as chemical dosing for pH and hardness adjustment.
Other crucial factors are membrane health (aging and fouling), energy efficiency (especially in RO and solar desalination), and overall plant maintenance and operational skills.

## Slide 4: Feed water Characteristics
Salinity:
The concentration of salts and pollutants in the feed water directly influences the efficiency and energy demands of the desalination process.
Temperature:
Feed water temperature affects membrane permeability and overall energy consumption, especially in RO and thermal systems.
Turbidity and Other Pollutants:
High levels of turbidity, COD, or BOD necessitate more intensive pre-treatment to prevent membrane fouling.

## Slide 5
Reverse Osmosis (RO):
Operating Pressure: High pressure is needed to overcome the osmotic pressure and push water through the semi-permeable membranes.
Membrane Properties: Factors like membrane aging, material, and fouling (biofouling, organic, colloidal) significantly impact efficiency and lifespan.
Energy Recovery Devices: Used in RO systems to capture energy from the high-pressure reject stream and reduce overall energy demand.
PROCESS-SPECIFIC PARAMETERS

## Slide 6: THERMAL DESALINATION (EVAPORATION):
Heat Loss Coefficient: Minimizing heat loss is crucial for thermal efficiency in processes like solar desalination.
Solar Insolation: A primary driver for solar-powered evaporation systems.
Freezing Point Parameters: In freezing-based desalination, factors like freezing temperature, subcooling, and initial salinity influence ice quality.

## Slide 7: POST-TREATMENT AND OPERATIONAL PARAMETERS
Chemical Dosing:
Adjusting pH, hardness, and alkalinity with chemicals like CO2 and sodium hydroxide is necessary after desalination to make water suitable for distribution.
Disinfection:
Dosing with disinfectants like sodium hypochlorite ensures water safety for consumption.
Maintenance and Cleaning:
Regular chemical and physical cleaning methods are required to address membrane fouling and scaling.
Control Systems:
Automated control mechanisms and skilled operators are essential for consistent performance and efficient operation.

## Slide 8: PH VALUE
A pH value measures the acidity or basicity of an aqueous solution on a scale of 0 to 14, where 7 is neutral, values below 7 are acidic, and values above 7 are basic. It is based on the concentration of hydrogen ions (H⁺), with lower pH indicating higher acidity and higher pH indicating greater basicity.
The recommended pH value for drinking water is generally between 6.5 and 8.5, a range supported by organizations like the World Health Organization (WHO) and the US Environmental Protection Agency (EPA).
Water outside this range may not only affect taste and cause plumbing issues, such as corrosion from low pH or scale buildup from high pH, but can also indicate the presence of contaminants.

## Slide 9: Factors influencing pH:
Natural processes: Geological features like limestone can increase water's alkalinity.
Human activities: Acid rain can lower pH levels, while other chemical activities can also influence it.
Water treatment: Municipalities treat water to ensure it falls within the safe range.
In summary, the 6.5 to 8.5 pH range is crucial for ensuring drinking water is safe, tastes good, and is not corrosive to plumbing systems.

## Slide 10: WHY THE 6.5 TO 8.5 RANGE MATTERS:
Acidic Water (below 6.5): Water that is too acidic can taste metallic and is corrosive, potentially dissolving toxic heavy metals like lead and copper from pipes into the water.
Neutral Water (around 7.0): This is considered pure water and is the center of the pH scale.
Alkaline Water (above 8.5): While not technically unsafe, water with a very high pH can have a strong smell and bitter taste, making it unpalatable. It can also lead to scale deposits in pipes.