## Slide 1: Nuclear Desalination

## Slide 2: Contents
Introduction & Status Economics
Safety Aspects Environmental Impact Questions & Discussion!

## Slide 3: Success Story on Nuclear Desalination:
Synergies in Nuclear desalination are a catalyst
for sustainable development
Aktau, 1961
Aktau, 1975
Water
Abstraction Purification Distribution Utilization Disposal
Energy
Fuel extraction and refining
Electricity
generation

## Slide 4: Introduction
& Status
Aktau, Kazakhstan
Ohi, Japan
Karachi, Pakistan
Kalpakkam, India

## Slide 5: Nuclear Desalination
Any co-located desalination plant that is powered with nuclear energy
1+1=2
1½
Viable option to meet:
Increasing global demand for water & energy
Concerns about climate change
Volatile fossil fuel prices
Security of energy supply
Cogeneration concept
Extra safety barriers
What is it?
Why?
How?

## Slide 6: Nuclear Desalination
Nuclear desalination is defined to be the production of potable water from seawater in a facility in which a nuclear reactor is used as the source of energy (electrical and/or thermal) for the desalination process.
All of the technologies currently in use for desalination require significant amounts of energy, either as low-temperature process heat or electricity.
Nuclear power plants can provide residual heat, low temperature steam and electricity.

## Slide 7: Nuclear Desalination Technology Sea water desalination with nuclear power
The coupling of two different technologies in a way that ensures the safe operation and the economic excellence of the overall plant Complex plant engineering and design
Water product
Safety isola
loop
Desalination plant therma consumption
Nuclear power plant
Desalination plant DDeesaslainlinataiotionnplpalantnt
Reverse OsmoMsuisltMi(REulfOtfie)SctaDgiestFilllastihon(M(MSFE)D)
Primary Energy
tion
l
Primary Energy
Electric Output

## Slide 8: Main Parameters in Desalination Processes
Capacity  Production of water (usually in m3/d)
Quality  Water quality expressed by amount of total dissolved solids (TDS) in
the product (in ppm)
Specific for thermal
Gain Output Ratio GOR  The ratio of the mass of water product per mass of steam needed. It is used as a measure of efficiency (the bigger the better)
Top Brine Temperature  The maximum temperature of the brine in the first stage/effect. Defines the quality of heat needed and affects GOR.
Specific for membrane
Pressure  The feedwater pressure used to pump the feedwater through the membrane. Usually related with the membrane type and mechanical properties.

## Slide 9: Main Desalination Technologies
In the MED process, vapor produced by an external heating steam source is multiplied by placing several evaporators (effects) in series under successively lower pressures, and using the vapor produced in each effect as a heat source for the next one.
Heating steam
seawater
Distilled water
Brine reject
Air extraction
P1>P2>P3
T1>T2>T3
GOR= Typical ~ 7 GORMax ~ 21 hybrid
1st Effect
2nd Effect
Multiple Effect Distillation (MED) Plant
3rd Effect
Plant
>90 C
or
<90 C

## Slide 10: Main Desalination Technologies
Multi-Stage Flash (MSF) Distillation Plant
MSF= evaporation and
condensation of water
GOR=8~10
20 stage MSF= 290 kJ/kg
In the MSF process, vapor is produced by heating the seawater close to its boiling temperature and passing it to a series of stages under successively decreasing pressures to induce flashing. The vapor produced is then condensed and cooled as distillate in the seawater tubes of the following stage.

## Slide 11: Main Desalination Technologies Reverse Osmosis (RO)
Seawater is forced to pass under pressure through special semi-permeable membranes: pure water is produced & brine is rejected.
The differential pressure must be high enough to overcome the natural tendency of water to move from the low salt concentration side to the high concentration side, as defined by osmotic pressure.
Operating pressure: 54 to 80 bar for seawater systems (Osmotic pressure ~ 25 bar for seawater )
The water recovery rate of RO systems tends to be low ~ 40%

## Slide 12: Main Desalination Technologies
 | Advantages | Weaknesses
MSF | Simplicity, reliability, long track record Minimum pretreatment Large unit sizes On-line cleaning | High energy requirements Not appropriate for single purpose plants
MED | Minimum pretreatment Low TDS product water Less electrical energy than MSF Lower capital cost than MSF | Complex to operate Small unit sizes
RO | Less energy needed than thermal Less feed water needed Lower capital costs | Extremely dependent on effectiveness of pretreatment More complex to operate than thermal Low product purity Boron issues to be addressed

## Slide 13: Coupling Nuclear Reactors with Desalination
13
Existing and planned nuclear power stations could be used to produce fresh water using the surplus of
Waste heat
MED desalination plants
  GT-MHR, through a flash tank using intercoolers reject heat
  HRT, using steam extractions
  PWR, using low pressure steam extraction
  AP1000, using condenser reject heat
  FPU, using condenser reject heat
MSF desalination plants
  BWR, through a flash tank using turbine steam extractions
Electricity
RO desalination plants
  Any plant (e.g., CANDU-6)
Hybrid (combination of heat and electricity)
  PHWR: steam extraction to MSF and electricity to RO

## Slide 14: Experience on Nuclear Desalination
Plant name | Location | Gross power [MW(e)] | Water capacity [m3/d] | Reactor type/ Desal. process
Shevchenko | Aktau, Kazakhstan | 150 | 80000 – 145000 | FBR/MSF&MED
Ikata-1,2 | Ehime, Japan | 566 | 2000 | LWR/MSF
Ikata-3 | Ehime, Japan | 890 | 2000 | LWR/RO
Ohi-1,2 | Fukui, Japan | 2 x 1175 | 3900 | LWR/MSF
Ohi-3,4 | Fukui, Japan | 1 x 1180 | 2600 | LWR/RO
Genkai-4 | Fukuoka, Japan | 1180 | 1000 | LWR/RO
Genkai-3,4 | Fukuoka, Japan | 2 x 1180 | 1000 | LWR/MED
Takahama-3,4 | Fukui, Japan | 2 x 870 | 1000 | LWR/RO
Diablo Canyon | San Luis Obispo, USA | 2 x 1100 | 2180 | LWR/RO
NDDP | Kalpakkam, India | 2 x 170 | 1800 | PHWR/RO
Karachi | Karachi, Pakistan | 175 | 1600 | MED

## Slide 15: Types of Nuclear Power Plants & Desalination Technologies used for Nuclear Desalination
Reactor type | Country | Desalination process | Status
LMFR | Kazakhstan | MED, MSF | Decommissioned (1999)
PWRs | Japan | MED, MSF, RO | Operating > 150 reactor-years
 | Korea, Argentina | MED, RO | Design stage
 | Russia | MED, RO | Design stage
PHWR | India | MSF, RO | Operating since (2002+2010)
 | Canada | RO | Design stage
 | Pakistan | MED | Operating since (2010)
BWR | Japan | MSF | Installed
HTGR | South Africa | MED, MSF, RO | Design stage
NHR | China | MED | Design stage

## Slide 16: Nuclear Desalination in Japan (8 units)
Ohi,
Kansai
Takahama, Kansai
Ikata, Shikoku
Photos are courtesy of EPCO
MED for in-plant water makeup
(1,000 m3/d)
MED for two PWR units
1,000 m3/d (each of 4 desalination units)
Kashiwazaki-Kariwa, Tokyo (BWR dismantled)
Genkai, Kyushu

## Slide 17: Nuclear Desalination in Pakistan
1600 m3/day MED Nuclear Desalination Demonstration Plant coupled with KANUPP(137MWe CANDU Reactor) commissioned in December, 2009.
First Phase:
MED : one-third capacity, first battery (1600 m3/day)
ICL & Sea water intake circuits: Full
capacity
Second Phase:
Second battery of MED plant (1600 m3/day) to be added(Locally designed and manufactured)

## Slide 18: Nuclear Desalination in India
NDDP: 6.3 MLD Sea water Desalination Plant at MAPS, Kalpakkam (Hybrid System)
Reverse Osmosis (RO): Commissioned in 2003
Capacity (MLD): 1.8
Product water quality (ppm): 500
Multi-Stage Flash (MSF):Commissioned in 2008-9
Capacity (MLD): 4.5
Product water quality (ppm): 10
Desalination plants coupled to a nuclear power plant(NPP).
One part follows RO with electricity from NPP.
Other part follows MSF distillation uses low grade heat from NPP. Two qualities of water are available which is blended for human or industrial consumption.
Presence of Radioactive Contaminants in product water: Nil

## Slide 19: Economics

## Slide 20: Harnessing Waste Heat for Nuclear Desalination
Improves overall efficiency
Improve economics
Can be used as Off-Peak Power
Electric Power
Nuclear Desalination?
Waste heat: Heat extracted from NPP with no penalty to the power production

## Slide 21: Harnessing Waste Heat PBMR for desalination
Using reject heat from the pre-cooler and intercooler of PBMR = 220 MWth at 70 °C + MED desalination technology
Cover the needs of 55,000 – 600,000 people
Desalinated water 15,000 –
30,000 m3/day
Waste heat can also be recovered from PWR and CANDU type reactors to preheat RO seawater desalination

## Slide 22: Cost of Nuclear Desalination
2.00
2.50
Nuclear + Fossil : RO Combined
Nuclear + MED
Cycle +
MED
Fossil : Standalone Combined oil fueled
MED
Water Cost ($/m3)
3.00
O&M Cost
Purchased Electricity cost
Electricity cost
Heat cost
Capital cost
1.50
1.00
0.50
0.00
Electricity needs
Cost assumptions:
optimal coupling between NPP and DP
Lifetime: 20 yrs Discount rate : 6%
SWRO : 5 kWh/m3 MSF : 3.0 kWh/m3 MED : 1.25 kWh/m3
Cycle + RO
WNA (2010), The Economics of Nuclear Power EIA (2010), Annual Energy Outlook 2011
Du and Parsons, (2009), Update on the cost of Nuclear Power, EIA, Annual Energy Outlook MIT, (2009), Update of the MIT 2003 Future of Nuclear Power Study
Economic Modelling Working Group (EMWG) of the GIF (2007), Cost Estimating Guidelines for Generation IV nuclear energy systems Rev 4.2
Global Water Intelligence (2010), Desalination Markets 2010 : Global Forecasts and analysis Global Water Intelligence (2011), IDA Desalination Plant Inventory
 | Capital Costs ($/kWe) | Fixed O&M ($/kW) | Variable O&M ($/MWh) | Fuel ($/MWh)
Nuclear | 4500 | 70 | 4 | 8
Coal | 2400 | 40 | 7 | 40
CCGT | 850 | 15 | 5 | 80
Wind | 2000 | 30 | 0 | 0
PV | 4000 | 25 | 0 | 0
It is important to incorporate enviro- economics when evaluating water and energy options
 a combination of environmental and
economic objectives

## Slide 23: Improvement of economics using Cogeneration 10% of 1000 MWe PWR for desalination
To produce 130 000 m3/day of desalinated water using 1000 MWe PWR Total revenue (Cogeneration 90% electricity +10% water):
 | Standalone | MED | RO
Electricity | 7166 M$ | 6771 M$ | 7062 M$
Water | 0 | 888 M$ | 672 M$
Total | 7166 M$ | 7660 M$ | 7700 M$
 |  | +7% | +7.5%
Using RO :
Increased availability
No lost power as in MED
Using waste heat to preheat feed water by 15oC increases water production by ~13%
Using MED:
Easier maintenance & pretreatment
Industrial quality water

## Slide 24: Water cost of small desalination plants
3.2% x 45%= 1.4% more steam needed in order to compensate the power lost
The energy costs of nuclear desalination ~15% of total electricity costs
Virtual free water
Nuclear PP 1000 MWe
MED - TVC
50,000 m3/d
GOR=10 150 ºC
3.2% of total steam flow
125 MW(th)
Steam extracted at 150 ºC from a NPP has produced 55% of its electricity potential.

## Slide 25: Safety Aspects

## Slide 26: Safety level of Nuclear Desalination
Safety issues of ND are similar to NPP
Safety: mainly dependent of nuclear plant, the design of coupling technology, and transient interactions between the two plants.
Additional specific safety considerations for the coupling schemes between the reactor and the desalination plant (DP):
Issues related to environment, shared resources, and siting…etc.

## Slide 27: Coupling
Coupling dictates specific safety considerations :
Prevent the transfer of radioactive materials from NPP to Desalination plant.
Minimize the impact of thermal desalination system on the nuclear
reactor
Protect the public and environment against radiation hazards that may be released from the Desalination plant system.
Specific requirements as dictated by the National Regulatory Body.
Backup heat or power source (NPP in refuelling).
Reactor
Loop
Isolation Heat Exchanger
Brine Heater
Desalination
Plant Loop
Isolation
Loop

## Slide 28: Safe coupling
3 physical safety barriers with the use of an
intermediate heat exchanger loop
Pressure Reversal
Online and batch monitoring of water radiation levels
2
4
6
1.7 bar
0.4 bar
0
Power Plant Secondary loop
5 bar
Intermediate loop
Desalination loop
1st barrier
2nd barrier
Turbine
HX
Experience has showed that radiation levels are orders of magnitudes below WHO specifications

## Slide 29: Coupling between NP and DP: Specific Safety Considerations
In case of coupling through the condenser, additional non-safety grade barriers are established (the main condenser tubes).
In normal operation: main condenser at lower pressure than its surroundings ( dynamic barrier)  No leakage
Radioactive releases to potable water can be prevented by design and operational provisions
IN CASE OF ACCIDENT CONDITIONS AT THE NP
ND is to be shut down  Prevent potential contamination Water produced by ND can be stored and monitored for radiological contamination before distribution

## Slide 30: Coupling between NP and DP: general considerations
Selection of proper technology
Required product quality & amount: power-to-water ratio Specific national requirements
Site selection
In-depth feasibility studies

## Slide 31: Coupling between NP and DP: technical considerations
Power vs. heating reactor Parallel vs. series cogeneration
Parallel cogen: part of steam to NP and part to DP
Series cogen: expanded steam from NP turbine continues to DP
At least 2 mechanical barriers between primary coolant and brine
DP backup heat source if NP is down
NP backup steam condenser if DP is down

## Slide 32: Additional considerations
Seawater Intake
Open intakes or sea wells
Concentrate disposal
temperature, salinity, chemicals
“Hybrid” systems
Combination of several desalination technologies
RO plus pure distillation water

## Slide 33: Environmental
Impact
Site Selection Coastal Impact Marine impacts Atmospheric Impacts

## Slide 34: Environmental Consideration
34
For Nuclear Desalination:
Environmental issues related to desalination are a major factor in
the design and implementation of desalination technologies.
For DP, major environmental issues are related to the disposal and management of the concentrate.
Typically a desalination plant concentrate consists of the following
components or groups of components, respectively :
high salinity (depends on the recovery rate);
heat (in thermal desalination);
Anti-scaling additives (poly-carbonic acids, polyphosphates);
antifoaming additives;
antifouling additives (mainly chlorine and hypochlorite);
halogenated organic compounds formed after chlorine addition;
acid;
corrosion products (metals).

## Slide 35: Environmental Aspects for Nuclear Desalination
ND
Impact
Marine
Nuclear Waste
Atmospheric
Site Selection Construction Land Use Visual
Costal
Intake
Discharge

## Slide 36: Site Selection
First step in planning a desalination plant is the selection of site, Among many factors affecting siting: Available energy, costs, transport of product water, discharge of brine, but also: the environmental impact of construction and operation of desalination plant.
Co-location with nuclear power offers partial mitigation of desalination’s impacts on the marine and coastal environment, increased economic competitiveness, and offers waste heat from the power plant as an energy source for the desalination process, thus reducing its global warming impact.
Co-location involves additional issues: e.g. high salinity and the chemical composition of the brine discharge.

## Slide 37: Coastal Impact
Land Use Example: Nuclear Desalination facilities of 100 000 m3/day would require 0.2 km2 12 to 510 MW of installed power – requiring co-located power generation | Method | Land use (km2) for 1 GWe power plant
 | Solar (photovoltaic) | 20 – 50
 | Wind | 50 – 150
 | Biomass (+ bio-alcohol/oil) | 4000 – 6000
 | Nuclear | 1 - 4
Source: IAEA; WEC, 2007 |  | 
Construction Impact
Smaller specific use of materials (tons/MW) + Smaller construction area,
Yet, Potential for longer construction period.
Visual Impacts
Serpa (P) solar power plant
Palm Springs (US) wind farm
Paluel (F) NPP

## Slide 38: Marine impacts
Entrainment and
impingement
Desalination impacts the marine environment through two major operation phases: seawater intake and effluent discharge.
Withdrawal needs for the Once-through cooling (OTC) for Nuclear are the highest
Possible environmental impacts of water intake
 | OTC | Cooling towers
Nuclear | 95 – 230 | 3 – 4
Fossil | 76 – 190 | 2
NG/Oil CC | 29 - 76 | 1
Strategies for Mitigation
Dry- and/or wet-cooling for Nuclear, and Indirect intake systems for desalination, or Intake from areas with low biological activity
Possible environmental impacts of discharge
Elevated temperature and salinity are aggravating marine life
Increased mortality or incapacitation
of marine organisms
Habitat deterioration or undesirable changes in species composition
Strategies for Mitigation
Commercial use of the discharged brine
Dilution with multi-port diffusers in biologically insensitive areas…
…and environmentally sound intakes!

## Slide 39: Atmospheric Impacts
Nuclear - MED
CCGT - MED
Oil - MED
Coal - MED
Nuclear - RO
CCGT - RO
Coal - RO
0
1
2
3
5
4
6
7
8
0.00
0.50
1.00
2.00
2.50
3.00
kgCO2eq/m3
1.50
Water Cost ($/m3)
Nuclear Desalination
lowest cost &emissions
Source: Analysis based on Primary Cost data from MIT (2009), EIA (2010), and GWI (2010)
It is important to incorporate enviro-economics when evaluating water and energy options
 a combination of environmental and economic objectives

## Slide 40: GHG Emissions of Nuclear
Desalination:

## Slide 41: Questions & Discussion!
Thank you!